## Slide 1: Internet of Things
LoRa and LoRaWAN
Mehdi Rasti
Amirkabir University of Technology

## Slide 2: Contents
Introduction
LoRa specification
Few use cases using LoRa technology
What is LoRa & LoRaWAN ?
LoRaWAN how IT works
LoRa protocol stack
LoRa modulated signal
  Basic modulation types
  Chirp spread spectrum (CSS)
  LoRaWAN frequencies
  Forward Error Correction & Coding RateChallenges
  Data rate
  SNR limit
LoRaWAN
LoRaWAN device classes
LoRa packert format
Time On Air
Adaptive Data Rate
Activation methods

## Slide 3: Refrencr
1. LoRa/LoRaWAN tutorial https://www.mobilefish.com/developer/lorawan/lorawan_quickguide_tutorial.html
2. Semtech: AN1200.22 - LoRa Modulation Basics (Revision 2, May 2015) https://www.semtech.com/uploads/documents/an1200.22.pdf
3. Semtech: SX1276/77/78/79 Datasheet (Rev. 5, August 2016) https://www.semtech.com/uploads/documents/DS_SX1276-7-8-9_W_APP_V5.pdf
4. Semtech: AN1200.13 - SX1272/3/6/7/8 LoRa Modem Design Guide (Revision 1, July 2013) https://www.semtech.com/uploads/documents/LoraDesignGuide_STD.pdf
5. LoRa Alliance, Inc: LoRaWAN specification https://lora-alliance.org/lorawan-for-developers
6. ETSI EN 300 220-2 (V3.2.1, June 2018) https://www.etsi.org/deliver/etsi_en/300200_300299/30022002/03.02.01_60/
en_30022002v030201p.pdf

## Slide 4: LoRa specification
• The LoRa wireless technology was developed by a French start-up company Cycleo which developed the LoRa modulation technology.
In 2012 the Semtech Corporation (NASDAQ: SMTC) acquired Cycleo.
The LoRa radio and modulation part is patented and its source is closed.
Semtech has licensed its LoRa intellectual property (ip) to other chip manufacturers, such as HopeRF, Microchip, Dorji, etc.
The word LORA is a trademark of Semtech Corporation, filed in 2015.
More information about Semtech: https://www.semtech.com/lora

## Slide 5: LoRa specification
The range between LoRa sender and receiver depends on the environment the equipment operates in. Indoor coverage largely depends on the type of building material used.
Environment | Range (km)
Urban areas (towns & cities) | 2-5
Rural areas (countrysides) | 5-15
Direct Line Of Sight | >15
Some notable records: Andreas Spiess, ground to ground connection: 212 km (= 131.73 miles) Weather balloon to ground connection: 702.67 km (= 436.61 miles)

## Slide 6: FEW USE CASES USING LORA TECHNOLOGY
• Smart utilities
Power transformer monitoring
Water level monitoring
Utility meter
Fuel monitoring (monitoring fuel levels in fuel tanks for heating houses)
•Health & Hygiene
Temperature / humidity monitoring
Environmental monitoring
Waste management (monitoring waste level in waste bins)

## Slide 7: FEW USE CASES USING LORA TECHNOLOGY
• Safety
Smart lightning
Water level monitoring
Radioactivity level monitoring
Dike monitoring (prevent peat dikes from drying out)
• Efficiency
Asset management (e.g. tracking containers, pallets, etc.)
Fleet management (e.g. tracking cars, vans, trucks, etc.)
• Agriculture
Monitoring animal welfare
Monitoring plant growing conditions

## Slide 8: What is LoRa & LoRaWAN ?
LoRa is an acronym for Long Range and it is a wireless technology where a low powered sender transmit small data packages (0.3 kbps to 5.5 kbps) to a receiver over a long distance.
A gateway can handle hundreds of devices at the same time.
The Things Gateway
(gateway / concentrator)
The Things Uno (end node)

## Slide 9: What is LoRa & LoRaWAN ?(END NODE)
A LoRa end node consists of 2 parts:
A radio module with antenna.
A microprocessor to process for example the sensor data.
End nodes are often battery powered.
A LoRa device (end node) has a wireless transceiver. If this device also has sensors, this device acts as a remote sensor. Such a device is called a mote, short for remote.
radio module
printed antenna
microprocessor

## Slide 10: What is LoRa & LoRaWAN ? (GATEWAY)
• A LoRa gateway consists of 2 parts:
• A radio module with antenna.
• A microprocessor to process the data.
• Gateways are mains powered and connected to the Internet.
• Multiple gateways can receive data from the same end node.
• The gateways can listen to multiple frequencies simultaneously,
in every spreading factor at each frequency.

## Slide 11: What is LoRa & LoRaWAN ?(LORAWAN NETWORK)
• LoRaWAN network architecture is deployed in a star topology.
• The communication between the end node and gateway is bidirectional which means the end node can send data to the gateway but it can also receive data from the gateway.

## Slide 12: LORAWAN HOW IT WORKS
• An end node broadcast its data to every gateway in its vicinity.
• The gateways forward this packet to the network server.
• The network server collects the messages from all gateways and filters out the
duplicate data and determines the gateway that has the best reception.
• The network server forwards the packet to the correct application server where the
end user can process the sensor data.
•Optionally the application server can send a response back to the end node.
When a response is send, the network server receives the response and determines
which gateway to use to broadcast the response back to the end node.

## Slide 13: DIRECT COMMUNICATION BETWEEN LORA DEVICES
• The LoRaWAN protocol does not support direct communication between end nodes.
• If you want direct communication between LoRa devices without the use of gateways, use the RadioHead Packet Radio library for embedded microprocessors. It provides a complete object-oriented library for sending and receiving packet sized messages via a variety of radios such as LoRa on a range of embedded microprocessors: https://www.airspayce.com/mikem/arduino/RadioHead/
• RadioHead does not have an official GitHub repo but several people have cloned the Radiohead library on GitHub.

## Slide 14: LORA PROTOCOL STACK

## Slide 15: LORA PROTOCOL STACK
• The LoRaWAN protocols are defined by the LoRa Alliance.
• It is a non-profit organisation of more than 500 member companies, committed to enabling large scale deployment of LPWAN IoT through the development and promotion of the LoRaWAN open standard.
• More information about the LoRa Alliance: https://lora-alliance.org/ , https://youtu.be/2Y0bMX3TVi0

## Slide 16: LORA MODULATED SIGNAL

## Slide 17: BASIC MODULATION TYPES
• As mentioned earlier an end node has a radio module. This radio module has a
modulator which encodes information onto a carrier signal.
• This modulated signal is transmitted and received by a gateway.
• The gateway also has a radio module. This radio module has a demodulator which
decodes the modulated signal and extracts the information.

## Slide 18: TRANSCEIVERS
• The communication between the end node and gateway is bidirectional which means the end node can send data to the gateway but it can also receive data from the gateway.
• If a device can both transmit and receive signals this device is also called a transceiver.
LoRa end nodes and gateways are transceivers.

## Slide 19: CHIRP SPREAD SPECTRUM (CSS)
• Besides the 3 basic modulation types there are many other modulation types.
• LoRa is a proprietary spread spectrum modulation scheme that is based on Chirp Spread Spectrum modulation (CSS).
• Chirp Spread Spectrum is a spread spectrum technique that uses wideband linear frequency modulated chirp pulses to encode information.
• Spread spectrum techniques are methods by which a signal is deliberately spread in the frequency domain. For example a signal is transmitted in short bursts, "hopping“ between frequencies in a pseudo random sequence.
• A chirp, often called a sweep signal, is a tone in which the frequency increases (upchirp) or decreases (down-chirp) with time.

## Slide 20: CHIRPS
Example of an up-chirp where the frequency increases in time.

## Slide 21: LORA MODULATED SIGNAL
• Another LoRa modulated signal example.

## Slide 22: LORA MODULATED SIGNAL
• The chirps are cyclically-shifted, and it is the frequency jumps that determines how the data is encoded onto the chirps, aka LoRa modulation.

## Slide 23: LORA MODULATED SIGNAL

## Slide 24: SYMBOL, SPREADING FACTOR AND CHIP
• A symbol represents one, or more bits of data, for example: Symbol = 1011111 (decimal = 95)
• In the example above the number of raw bits that can be encoded by the symbol is 7. This is the same as saying: Spreading Factor (SF) = 7
• The symbol has 2SF values. If SF=7, the values ranges from 0 - 127. The symbol value is encoded onto a sweep signal (up-chirp).

## Slide 25: SYMBOL, SPREADING FACTOR AND CHIP
• Another example, lets assume SF=12 Each symbol can carry 12 raw bits of information and there are 212 = 4096 unique chip values ranging from 0 to 4095.
• The Spreading Factor (SF) defines two values:
- The number of raw bits that can be encoded by that symbol: SF
- Each symbol can hold 2SF chips
• Please be aware of the difference between a chirp and a chip.
A symbol holds 2SF chips.
Chirps are simply a ramp from flow to fhigh (up-chirp) or fhigh to flow (down-chirp).

## Slide 26: LORAWAN FREQUENCIES
• As mentioned before LoRaWAN uses frequencies in the ISM band.
•On The ThingsNetwork (TTN) website you can find the (carrier) frequencies for your country.
• First find the frequency plan which applies to your country: https://www.thethingsnetwork.org/docs/lorawan/frequencies-by-country.html
Forexample: Netherlands uses frequency plan: EU863-870 (Note: EU433 is not implemented, please ignore it.)
• If you know your frequency plan, find the corresponding LoRaWAN frequencies: https://www.thethingsnetwork.org/docs/lorawan/frequency-plans.html

## Slide 27: EU863-870 ISM BAND CHANNEL FREQUENCIES
LoRaWan frequencies used in Europe, for example in the Iran (TTN freq. plan: EU863-870) Channel Uplink freq (MHz)

## Slide 28: EU863-870 ISM BAND CHANNEL FREQUENCIES
If your country uses the EU863-870 ISM band, than according to the LoRaWAN
Regional Parameters document every EU868MHz end device must implement the
following default channels:
- 868.10 MHz, bandwidth = 125 kHz
- 868.30 MHz, bandwidth = 125 kHz
- 868.50 MHz, bandwidth = 125 kHz
and additional 5 frequencies.
The other 5 frequencies can be freely attributed by the network operator. For example, The Things Network implemented the following frequencies: 867.1, 867.3, 867.5, 867.7 and 867.9.

## Slide 29: ETSI SUB BANDS 863-870
ETSI divides the 863-870 MHz band (referenced “G”) into 5 sub-bands: G, G1, G2, G3 and G4. [5]
Each sub band has different constraints in term of EIRP, duty cycle and channel bandwidth.

## Slide 30: EU863-870 FREQUENCIES AND SUB BANDS

## Slide 31: BANDWIDTH
LoRaWAN only uses the following bandwidth ranges: 125 kHz, 250 kHz and 500 kHz. Which of these 3 ranges are actual used depends on the region or frequency plan. For example in Europe only the bandwidths 125kHz and 250 kHz are used.
The relationship between bandwidth and carrier frequency can be seen in the figure below.

## Slide 32: CARRIER FREQUENCIES & BANDWIDTHS

## Slide 33: CHANGING FREQUENCIES FOR EVERY TRANSMISSION
An end device changes channel in a pseudo-random fashion for every transmission. Changing frequencies makes the system more robust to interferences.
For example in Europe for uplink transmissions 8 different frequencies are used.

## Slide 34: DWELL TIME & HOP TIME
Dwell time (or transmit time) is the amount of time needed to transmit on a frequency.
Hop time is the amount of time needed to change from one frequency to another in which the radio is not transmitting

## Slide 35: ISM BAND AND DUTY CYCLE
In Europe when using the ISM band frequencies (863 MHz - 870 MHz) users must comply to the following rules:
For uplink, the maximum transmission power is limited to 25mW (14 dBm). For downlink (for 869.525MHz), the maximum transmission power is limited to 0.5W (27 dBm)
There is an 0.1% and 1.0% duty cycle per day depending on the channel.
Besides these ISM band rules, the network operator (for example The Things Network) can also add additional restrictions.

## Slide 36: TIME ON AIR
When a signal is send from a sender it takes a certain amount of time before a receiver receives this signal. This time is called Time on Air (ToA).

## Slide 37: TIME ON AIR
Duty cycle is the proportion of time during which a component, device, or system is operated. The duty cycle can be expressed as a ratio or as a percentage.
As mentioned previously in Europe there is a 0.1% and 1.0% duty cycle per day depending on the channel.

## Slide 38: DUTY CYCLE

## Slide 39: Forward Error Correction & Coding Rate
Forward Error Correction (FEC) is the process where error correction bits are added to the transmitted data.
These redundant bits helps to restore the data when the data gets corrupted by interference.
If more error correction bits are added, the easier the data can be corrected.
However by adding more error correction bits, more data is transmitted which decreases the battery life.

## Slide 40: Forward Error Correction & Coding Rate
The coding rate refers to the proportion of the transmitted bits that actually carries
information.
LoRa allowed coding rate values: CR = 4/5, 4/6, 4/7 or 4/8. Another notation:
CR = 4 / (4 + CR) where CR = 1,2,3,4

## Slide 41: CODING RATE
For example, SF = 8 (the transmitted bits = 8)

## Slide 42: CHIP RATE
The unit of bandwidth (BW) is Hertz (Hz) which is the number of vibrations or wave cycles per second. This bandwidth is interchangeably with chip rate: BW = Rc = chip rate (chips/s) [1]
For example: BW=125 kHz BW = Rc = 125000 chips/s

## Slide 43: SYMBOL RATE
The Symbol Rate (Rs) is calculated as follow: Rs (symbols/sec) = BW / 2SF = Rc / 2SF [1] Bandwidth (BW) in Hz Spreading Factor (SF): 7-12
For example: BW=125 kHz, SF=7 Rs = 125000 / 27 = 977 symbols/sec

## Slide 44: DATA RATE
The chip rate is always higher than the symbol rate: Rc > Rs
To calculate the data rate (DR) or bit rate (Rb):
Bandwidth (BW) in Hz
Spreading Factor (SF): 7-12
Code Rate (CR): 1-4

## Slide 45: DATA RATE
For example: SF=7, CR=1
BW=125 kHz, Rb = 7 x (125000 / 27) x (4 / (4 + 1)) = 5.5 kbits/s
BW=250 kHz, Rb = 7 x (250000 / 27) x (4 / (4 + 1)) = 10.9 kbits/s
BW=500 kHz, Rb = 7 x (500000 / 27) x (4 / (4 + 1)) = 21.9 kbits/s
If you increase the bandwidth, the bit rate or data rate is increased.

## Slide 46: CHIP DURATION
Because Rc = BW [1], the chip duration is calculated as follow:
Tc (sec) = 1 / BW
Bandwidth (BW) in Hz
For example: BW=125 kHz Tc = 1 / 125000 = 8 μs

## Slide 47: SYMBOL DURATION
For example: SF7
BW=125 kHz, Ts = 27 / 125000 = 1.024 ms
BW=250 kHz, Ts = 27 / 250000 = 512 μs
BW=500 kHz, Ts = 27 / 500000 = 256 μs
If the BW increases, the Symbol duration decreases.
For example: BW=125 kHz
SF=7, Ts = 27 / 125000 = 1.024 ms
SF=9, Ts = 29 / 125000 = 4.096 ms
SF=12, Ts = 212 / 125000 = 32.768 ms
If the SF increases, the Symbol duration increases.

## Slide 48: SPREADING FACTOR VS SYMBOL DURATION
An overview of symbol durations with respect to different Spreading Factors.
If the SF increases by one the symbol duration doubles.

## Slide 49: SPREADING FACTOR IMPACT
If you increase the SF by 1:
The symbol duration or sweep time doubles compared to the previous SF.
It reduces the bit rate approximately by half compared to the previous SF.
The Time on Air (ToA) (=message transmission time) increases which means the distance increases.
To give you an idea what the Time on Air is for a 10 byte payload, BW=125kHz:
SF7, transmission time = 41 ms
SF12, transmission time = 991 ms
LoRa devices uses a higher spreading factor when the signal is weak or there is lot of interference. Using a higher spreading factor means a longer Time on Air (ToA).
If an end device is further away from a gateway the signal get weaker and therefore needs a higher spreading factor.

## Slide 50: SNR LIMIT
For each spreading factor there is a SNR limit, if this limit is reached the receiver will not be able to demodulate the signal.

## Slide 51: SNR LIMIT
In the table below, the SNR limit can be found for each Spreading Factor:
Note: If the SF increases by 1, the SNRlimit changes by -2.5 dB

## Slide 52: RECEIVER SENSITIVITY
To calculate the receiver sensitivity:
S = -174 + 10xlog10(BW) + NF + SNRlimit
Receiver sensitivity (S) in dBm
Bandwidth (BW) in Hz
Receiver Noise Figure (NF) in dB
NF is fixed for a given hardware implementation
For LoRa end node transceiver chips SX1272 and SX1276
use NF = 6 dB
Signal-to-Noise limit (SNRlimit) in dB
For example: BW=125kHz, NF=6dB Lets calculate the receiver sensitivity for SF 7-12. Use the SNRlimit from the previous table.

## Slide 53: RECEIVER SENSITIVITY
SF=7: SNRlimit=-7.5dB
S = -174 + 10xlog10(125000) + 6 -7.5 = -125 dBm SF=8: SNRlimit=-10dB
S = -174 + 10xlog10(125000) + 6 -10 = -127 dBm SF=9: SNRlimit=-12.5dB
S = -174 + 10xlog10(125000) + 6 -12.5 = -130 dBm SF=10: SNRlimit=-15dB
S = -174 + 10xlog10(125000) + 6 -15 = -132 dBm SF=11: SNRlimit=-17.5dB
S = -174 + 10xlog10(125000) + 6 -17.5 = -135 dBm SF=12: SNRlimit=-20dB
S = -174 + 10xlog10(125000) + 6 -20 = -137 dBm

## Slide 54: RECEIVER SENSITIVITY

## Slide 55: RECEIVER SENSITIVITY
If the distance between end node and gateway increases the signal gets weaker and therefore an increase spreading factor is needed for a lower receiver sensitivity to be able to demodulate the received signal. The Spreading Factor ranges from 7 when close to a gateway to 12 when far away from a gateway.

## Slide 56: LoRaWAN

## Slide 57: LORAWAN DEVICE CLASSES
The LoRaWAN specification defines three device classes:

## Slide 58: CLASS A
At any time an end node can broadcast a signal. After this uplink transmission (tx) the end node will listen for a response from the gateway.
The end node opens two receive slots at t1 and t2 seconds after an uplink transmission. The gateway can respond within the first receive slot or the second receive slot, but not both.
Class B and C devices must also support class A functionality.

## Slide 59: CLASS B
In addition to Class A receive slots, class B devices opens extra receive slots at scheduled times.
The end node receives a time synchronised beacon from the gateway, allowing the gateway to know when the node is listening.
A class B device does not support device C functionality.

## Slide 60: CLASS C
In addition to Class A receive slots a class C device will listen continuously for responses from the gateway.
A class C device does not support device B functionality.

## Slide 61: LORA PACKET FORMAT
The LoRa packet comprises of three elements: Preamble, header (optional) and payload.

## Slide 62: LORA PACKET FORMAT
There are two types of LoRa packet format modes:
The explicit header mode includes a short header that contains information about the payload length, coding rate and whether a CRC is used in the packet.CRC stands for Cyclic Redundancy Check and is used to detect errors in digital data.
The implicit header mode where the payload, coding rate and CRC presence are fixed. In this mode the header is removed from the packet thus reducing transmission time. In this case the payload length, error coding rate and presence of the payload CRC must be manually configured on both sides of the radio link.

## Slide 63: LORA PACKET FORMAT
The preamble is used to detect the start of the packet by the receiver.
The header (only in explicit header mode) is the default mode of operation. It provides information on the payload:
- The payload length in bytes.
- The forward error correction code rate.
- The presence of an optional 16 bits CRC for the payload.
The payload is a variable-length field that contains the actual data coded at the forward error correction code rate either as specified in the header in explicit mode or fixed in implicit mode. An optional payload CRC may be appended.

## Slide 64: TIME ON AIR
When a signal is send from a sender it takes a certain amount of time before a receiver receives this signal.
This time is called Time on Air (ToA).

## Slide 65: TIME ON AIR
The total air transmission time of a LoRa packet, aka Time on Air (ToA), aka LoRa
packet duration (Tpacket) is calculated as follow:
ToA = Tpacket = Tpreamble + Tpayload
Preamble duration (Tpreamble) in sec
Payload duration (Tpayload) in sec
The preamble duration is calculated as follow:
Tpreamble = (npreamble + 4.25) Ts
Number of preambles
For EU868: npreamble = 8 symbols
Symbol duration (Ts) in sec

## Slide 66: TIME ON AIR
The payload duration (Tpayload) is calculated as follow:
Tpayload = Ts(8+max(ceil((8PL-4SF+28+16CRC-20H)/4(SF-2DE)) (CR+4),0))
Symbol duration (Ts) in sec
Payload (PL) in bytes
Spreading Factor (SF=7-12)
CRC (enabled=1, disabled=0. For LoRaWAN default CRC=1)
Header (disabled H=1 [implicit], enabled H=0 [explicit])
For LoRaWAN header is enabled: H=0
LowDataRateOptimize (enabled DE=1, disabled DE=0)
Coding rate (CR=1,2,3 or 4. For LoRaWAN default CR=1)

## Slide 67: LOW DATA RATE OPTIMIZATION
Given the potentially long duration of the packet at high spreading factors the Low Data Rate Optimization (LowDataRateOptimize) option can be set to improve the robustness of the transmission to variations in frequency over the duration of the packet transmission and reception.
When the Low Data Rate Optimization is enabled it increases the robustness of the LoRa link at these low effective data rates. Its use is mandated when the symbol duration exceeds 16ms. Note that both the transmitter and the receiver must have the same setting for LowDataRateOptimize.
The LowDataRateOptimize is enabled for bandwidth 125 kHz and Spreading Factor >= 11

## Slide 68: TIME ON AIR
An online tool to calculate the Time on Air see: https://www.loratools.nl/#/airtime
For example: npreamble = 8, explicit header=enabled, CRC=enabled, payload length=10 bytes, CR=1 and BW=125 kHz

## Slide 69: TIME ON AIR

## Slide 70: TIME ON AIR
A higher spreading factor means a longer Time on Air and a lower data rate as can be seen in the previous graph.
A higher spreading factor also means the sender-receiver range gets larger but it requires more energy (battery power).

## Slide 71: ADAPTIVE DATA RATE
The LoRaWAN protocol defines the Adaptive Data Rate (ADR) scheme to control
the uplink transmission parameters of LoRa devices:
- Spreading Factor (SF)
- Bandwidth (BW) Transmission parameters
- Transmission power
Whether the ADR functionality will be used is requested by the end nodes by setting the ADR flag in the uplink message. If the ADR flag is set, the network server can control the end node’s transmission parameters.
ADR should only be used in stable Radio Frequency (RF) situations where end nodes do not move. Mobile end nodes which are stationary for longer times can enable ADR during those times.

## Slide 72: ACTIVATION METHODS
An end device must first be activated before it is able to communicate with the network server.
There are two methods to activate an end device in a LoRaWAN network:
- Over-The-Air-Activation (OTAA)
- Activation-By-Personalisation (ABP)
Both methods will be explained next, but please be aware that it is a simplified explanation. If you need a detailed explanation please read the LoRaWAN 1.0.2 specification.

## Slide 73: OTAA
In OTAA, a device is given a DevEUI, an AppEUI and an AppKey. Confusingly enough, the AppKey is used to generate the session keys, NwkSKey and AppSKey.
To activate, the device sends a join request and uses the join response to derive the session keys NwkSKey and AppSKey
The device may store those keys and continue to use them to communicate. If they are lost or the network chooses to expire them, the device must re-join to generate new keys.

## Slide 74: OTAA
Pros:
Session keys are only generated when required, so cannot be compromised prior to activation.
If the device changes to a new network, it can re-join to generate the new keys - rather than having to be re-programmed.
Network settings like RxDelay and CFList can be specified at join time.
Cons:
A scheme is required to pre-program each device with a unique DevEUIand AppKey, and the correct AppEUI.
The device must support the join function and be able to store dynamically generated keys.

## Slide 75: ABP
In ABP (Activation By Personalisation), a device does not need a DevEUI, an AppEUI or an AppKey.
Instead the session keys NwkSKey and AppSKey are preprogrammed into the device and the device is pre-registered on the network.
When the device wants to communicate, it does so using the session keys without having to use a join procedure first.

## Slide 76: ABP
Pros:
The device does not need the capability or resources to perform a join procedure.
The device does not need to decide whether a join is necessary at any point, since it is never necessary.
No scheme is necessary to specify a unique DevEUI or AppKey
Cons:
the scheme must be secure to prevent the keys being obtained or derived by rogue parties. • If the device is compromised at any time, even before activation, the keys may be discovered.
Network settings cannot be specified at join time.
Events that warrant a change of keys (for example, moving to a new network, the device being compromised, or the keys being expired) require a re-programming of the device..

## Slide 77: ?